## Slide 1
ME 165
Basic Mechanical Engineering
Lecture 8
Kinematics of Particles
Sadia Tasnim
Lecturer
Department of Mechanical Engineering, BUET

## Slide 2
Introduction of Dynamics
Engineering Mechanics
Statics: Study of bodies in equilibrium
Dynamics: Study of motion
1. Kinematics: concerned with geometric aspects of motion, e.g. s, v, a and t
2. Kinetics: concerned with
how forces causing the motion
Newton’s 2nd Law: 𝑭𝑅 = 𝑚𝒂
Newton’s 1st Law:
𝑭𝑅 = 0

## Slide 3
Kinematics: concerned with geometric aspects of motion, e.g. s, v, a and t
𝑡 = 0
𝑡
𝑡 + 𝑑𝑡
𝑠
𝑠 + 𝑑𝑠
𝒗 =
𝒅𝒔
𝒅𝒕
𝒅𝒗 𝒅𝟐𝒔
𝒂 = =
𝒅𝒕 𝒅𝒕𝟐
shown as scalars for a simpler demonstration
Introduction of Dynamics

## Slide 4
𝟏. 𝒗 =
𝒅𝒕
𝒅𝒗
𝟐. 𝒂 =
𝒅𝒕
𝑡 = 0
𝑡
𝑡 + 𝑑𝑡
𝑠
𝑠 + 𝑑𝑠
𝟑. 𝑭 = 𝒎𝒂
𝟒. 𝒔 = 𝒓𝜽
Note: only scalar equations are shown from here on for simplification purpose
Introduction of Dynamics
𝒅𝒔

## Slide 5
Rectilinear Motion
𝒙(𝒕): function of time
𝑡1
𝑡2
O
𝑥1
𝑥2
−𝑥1
𝑣1
𝑣2
Instantaneous velocity ,
Instantaneous acceleration ,
𝒙 = 𝒙𝟎 + 𝒗𝒄𝒕
𝒗 =
𝒙 =
=
Uniform Rectilinear Motion
Uniformly Accelerated Rectilinear Motion

## Slide 6
Curvilinear Motion
The motion of a particle follows a curved path.
𝒓 = 𝑥𝒊 + 𝑦𝒋 + 𝑧𝒌
∆𝑡→0 Δ𝑡
𝒗 = lim Δ𝒓 = 𝑑𝒓
𝑑𝑡
∴ 𝒗 = 𝒊 + 𝐣 + 𝒌 = 𝑣𝑥𝒊 + 𝑣𝑦𝒋 + 𝑣𝑧𝒌
𝒓 𝑡 : 𝑓𝑢𝑛𝑐𝑡𝑖𝑜𝑛 𝑜𝑓 𝑡𝑖𝑚𝑒
∆𝒓 = 𝒓′ − 𝒓
tangent to path
𝑥𝒊
𝑧𝒌
𝒓
𝑃(𝑥, 𝑦, 𝑧)
𝑃′(𝑥′, 𝑦′, 𝑧′)
∆𝒓
𝒓′
𝑦𝒋
∴ 𝒂 = 𝒊 + 𝒋 + 𝒌 = 𝑎𝑥𝒊 + 𝑎𝑦𝒋 + 𝑎𝑧𝒌

## Slide 7
g
Motion with constant acceleration:
𝟏
𝟐
𝒔 = 𝒔𝟎 + 𝒗𝟎𝒕 + 𝟐 𝒂𝒄𝒕
𝒗 = 𝒗𝟎 + 𝒂𝒄𝒕
𝟎
𝟐 𝟐
𝒗 = 𝒗 + 𝟐𝒂
𝒄
𝒔 − 𝒔𝟎
y
x
O
𝑃(𝑥0, 𝑦0)
(𝒗0)𝑥
(𝒗0)𝑦
@ 𝑡𝑖𝑚𝑒 𝑡
𝑃(𝑥, 𝑦)
𝒗
𝒗𝑥
𝒗𝑦
Motion of a Projectile

## Slide 8
Horizontal motion:
𝑎𝑥 = 𝑎𝑐 = 0
𝑥 = 𝑥0 + (𝒗0)𝑥𝑡
𝒗𝑥 = (𝒗0)𝑥
Vertical motion:
𝑎𝑦 = 𝑎𝑐 = −𝑔
1
y = 𝑦0 + (𝒗0)𝑦𝑡 − 2 𝑔𝑡
2
𝒗𝑦 = (𝒗0)𝑦−𝑔𝑡
0 𝒚
𝒗𝑦𝟐 = (𝒗 )𝟐−2𝑔 𝒚 − 𝒚
𝟎
x
O
𝑃(𝑥0, 𝑦0)
(𝒗0)𝑥
(𝒗0)𝑦
@ 𝑡𝑖𝑚𝑒 𝑡
𝑃(𝑥, 𝑦)
𝒗
𝒗𝑥
𝒗𝑦
Note: Horizontal motion and vertical motion take
place during the same time.
y
Motion of a Projectile

## Slide 9
Problem:
A basketball player shoots when she is 16 ft from the backboard. Knowing that the ball has an initial velocity 𝒗0 at an angle of 30° with the horizontal, determine the value of 𝒗0 when d =9 in.
Motion of a Projectile

## Slide 10: Motion of a Projectile
Solution:
Horizontal motion: 𝒙 = 𝒙𝟎 + (𝒗𝟎)𝒙𝒕
At B, 16 − 𝑑 = 0 + (𝒗𝟎 cos 30° × 𝑡𝐵)
𝐵
⇒ 𝑡 =
16−𝑑
𝒗𝟎 cos 30°
𝟏
Vertical motion: 𝒚 = 𝒚𝟎 + (𝒗𝟎)𝒚𝒕 − 𝟐 𝒈𝒕
𝟐
𝐵
1
At B, 3.2 = 0 + 𝒗𝟎 sin 30° × 𝑡𝐵 − × 32 × 𝑡2
𝟎
⇒ 3.2 = 0 + 𝒗 sin 30° ×
2
16−𝑑
𝒗𝟎 cos 30°
2
− 1 × 32 × (
16−𝑑
𝒗𝟎 cos 30°
)2
0
⇒ 𝑣2 =
2𝑔(16−𝑑)2
3[ 1 16−𝑑 −3.2]
3
∴ 𝒗𝟎 = 𝟐𝟗. 𝟖 𝒇𝒕/𝒔
7 ft
3.2 ft
16

## Slide 11
Relative Position:
𝒙𝐵/𝐴 = 𝒙𝐵 − 𝒙𝐴
Relative Velocity:
𝒗𝐵/𝐴 = 𝒗𝐵 − 𝒗𝐴
Relative Acceleration:
𝒂𝐵/𝐴 = 𝒂𝐵 − 𝒂𝐴
⇒ 𝒙𝐵 = 𝒙𝐴 + 𝒙𝐵/𝐴
⇒ 𝒗𝐵 = 𝒗𝐴 + 𝒗𝐵/𝐴
⇒ 𝒂𝐵 = 𝒂𝐴 + 𝒂𝐵/𝐴
A
B
O
𝑥𝐴
𝑥𝐵
𝑥𝐵/𝐴
Relative Motion

## Slide 12
x
y
z
O
Fixed Reference Frame
A
B
𝒓
𝐵
x'
𝒓𝐴
y'
z'
O
Translating Frame
𝒓𝐵/𝐴
𝒓𝐴 and 𝒓𝐵 are absolute positions
𝒓𝐵/𝐴 is relative position of B relative to A.
𝒓𝐵/𝐴 = 𝒓𝐵 − 𝒓𝐴
Relative Position:
𝒓𝐵/𝐴 = 𝒓𝐵 − 𝒓𝐴
⇒ 𝒓𝐵 = 𝒓𝐴 + 𝒓𝐵/𝐴
Relative Velocity:
𝒗 = 𝒗 − 𝒗
𝐵/𝐴 𝐵 𝐴
⇒ 𝒗𝐵 = 𝒗𝐴 + 𝒗𝐵/𝐴
Relative Acceleration:
𝒂𝐵/𝐴 = 𝒂𝐵 − 𝒂𝐴
⇒ 𝒂𝐵 = 𝒂𝐴 + 𝒂𝐵/𝐴
Motion Relative to Frame in Translation

## Slide 13
Problem:
Three seconds after automobile B passes through the intersection shown, automobile A passes through the same intersection. Knowing that the speed of each automobile is constant, determine (a) the relative velocity of B with respect to A, (b) the change in position of B with respect to A during a 4-s interval, (c) the distance between the two automobiles 2 s after A has passed through the intersection.
Relative Motion

## Slide 14
Problem:
Conveyor belt A, which forms a 20° angle with the horizontal, moves at a constant speed of 4 ft/s and is used to load an airplane. Knowing that a worker tosses duffel bag B with an initial velocity of 2.5 ft/s at an angle of 30° with the horizontal, determine the velocity of the bag relative to the belt as it lands on the belt.
Relative Motion

## Slide 15
O
𝑥𝐴
𝑥𝐵
𝑙𝑠𝑒𝑚𝑖
Datum
⇒ 𝑥𝐴 + 𝑥𝐵 = C
⇒
𝑑(𝑥𝐴 + 𝑥𝐵) 𝑑
𝑑𝑡 𝑑𝑡
= (𝐶)
⇒ 𝑎𝐴 = −𝑎𝐵
Dependent Motion
𝑥𝐴 + 𝑙𝑠𝑒𝑚𝑖 + 𝑥𝐵 = 𝑙𝑇
⇒
⇒ 𝑣𝐴 = −𝑣𝐵
⇒

## Slide 16: Dependent Motion
Problem:
Collar A starts from rest and moves upward with a constant acceleration. Knowing that after 8 s the relative velocity of collar B with respect to collar A is 24 in./s. Determine-
the accelerations of A and B,
the velocity and the change in position of B after 6 s.
9

## Slide 17: Dependent Motion
Solution:
𝟐𝒚𝑨 + 𝒚𝑩 + 𝒚𝑩 − 𝒚𝑨
= 𝒄𝒐𝒏𝒔𝒕𝒂𝒏𝒕
⇒ 𝒚 + 𝟐𝒚
𝑨 𝑩
= 𝒄𝒐𝒏𝒔𝒕𝒂𝒏𝒕
𝑨 𝑩
𝟏
So, 𝒗 + 𝟐𝒗 = 𝟎 and (a)
Now, 𝒗𝐴 = (𝒗0)𝐴+𝒂𝑨𝑡 = 𝒂𝑨𝒕
and 𝒗𝐵 = (𝒗0)𝐵+𝒂𝑩𝑡 = 𝒂𝑩𝒕
Here, 𝒗𝐵/𝐴 = 𝒗𝐵 − 𝒗𝐴 =
𝟑
𝒂𝑩 − 𝒂𝑨 𝒕 = − 𝟐 𝒂𝑨𝒕
𝟑
⇒ 𝟐𝟒 = − 𝒂𝑨 × 𝟖
𝟐
𝒊𝒏 𝒊𝒏
⇒ 𝒂𝑨 = −𝟐 𝒔𝟐 = 𝟐 𝒔𝟐
∴ 𝒂
𝑩
= 𝟏 𝒊𝒏
𝒔𝟐
(b) 𝒗𝐵 = 𝒂𝑩𝒕 = 𝟏 × 𝟔 = 𝟔 𝒊𝒏/𝒔
𝟏
𝒚𝑩 = (𝒚0)𝐵+(𝒗0)𝐵𝒕 + 𝟐 𝒂𝑩𝒕
𝟐
∴ 𝒚𝑩 −
𝒚𝟎 𝑩 = 𝟏𝟖 𝒊𝒏
0
𝒂𝑨 + 𝟐𝒂𝑩 = 𝟎 ⇒ 𝒂𝑩 = − 𝟐 𝒂𝑨
0
10
𝑦𝐴
𝑦𝐵
+

## Slide 18
Newton’s 2nd Law of Motion
𝑑𝒗 𝑑
= 𝑚𝒂 = 𝑚 =
𝑑𝑡 𝑑𝑡
𝑑𝑡
𝑑𝑳
𝑚𝒗 = = 𝑳
Here, 𝑳 = 𝑚𝒗 is the linear momentum of particle
= 𝑚𝒂
Equation of motion
Kinetic diagram
inertia force
Accelerated motion
The acceleration of the movement of an object is proportional to the resultant force and is also in the same direction of the resultant force.

## Slide 19
Equation of Motion: Rectangular Co-ordinates
3D
2D
= 𝑚𝒂

## Slide 20
Curvilinear Motion: Tangential & Normal Components
2D Plane
Osculating plane
t
n

## Slide 21
Curvilinear Motion: Tangential & Normal Components
𝒗 = 𝑣𝒖𝑡
𝒂 = 𝑎𝑡𝒖𝑡 + 𝑎𝑛𝒖𝑛
Here,
𝑎 = 𝑎2 + 𝑎2
𝑡 𝑛

## Slide 22
𝑬𝒒𝒏 of Motion: Tangential & Normal Components
𝒂𝑛
𝒂𝑡
= 𝑚𝒂

## Slide 23
Laws of Dry Friction
Impending motion
F
Always tangent to contact surface and opposite to impending motion
F
P
Limiting static frictional force
Motionless
(static)
Motion (kinetic)
𝑭𝒎 = µ𝒔𝑵
Kinetic frictional
force
𝑭𝒌 = µ𝒌𝑵

## Slide 24
Problem:
The two blocks shown starts to move from the rest. The coefficients of friction between blocks and the inclines are 𝜇𝑠 = 0.25 and 𝜇𝑘 = 0.20. Neglecting the masses of the pulleys, determine-
(a) the acceleration of each block and (b) the tension in the cable.
Equation of Motion

## Slide 25: Equation of Motion
9
Solution:
𝑥𝐴
𝑥𝐵
Kinematics: 𝑥𝐴 + 2𝑥𝐵 = 𝐶
Change in position:
1 1
1
∆𝑥𝐴 + 2∆𝑥𝐵= 0
⇒ ∆𝑥𝐵= − 2 ∆𝑥𝐴 = 2 ∆𝑥𝐴 (𝑚𝑎𝑔𝑛𝑖𝑡𝑢𝑑𝑒)
1
⇒ 𝑥𝐵 = 2 𝑥𝐴
∴ 𝑎𝐵 = 2 𝑎𝐴------ (1)